## Slide 1
Chapter 4
Assignment of byte addresses
Byte addressing refers to hardware architectures which support accessing individual bytes of data rather than only larger units called words, which would be word-addressable.
The basic unit of digital storage is called a bit. In most common computer architectures, 8 bits are grouped together to form a byte
BaroAqoon.com

## Slide 2
Word size (Word length) – The maximum number of bits of data that the CPU can process at one time (8 bits, 16 bits, 32 bits, or 64 bits)
Word size or Word length
BaroAqoon.com

## Slide 3
Little Endian (e.g., in DEC, Intel)
» low order byte stored at lowest address
» byte0 byte1 byte2 byte3
Example
BaroAqoon.com

## Slide 4
Big Endian
• Big Endian (e.g., in IBM, Motorolla, Sun, HP)
» high order byte stored at lowest address
» byte3 byte2 byte1 byte0
• Programmers/protocols should be careful
when transferring binary data between Big
Endian and Little Endian machines
BaroAqoon.com

## Slide 5
• In case of 16 bit data, aligned words begin at
byte addresses of 0,2,4,……………………
• In case of 32 bit data, aligned words begin at
byte address of 0,4,8,………………………
• In case of 64 bit data, aligned words begin at
byte addresses of 0,8,16,…………………...
• In some cases words can start at an arbitrary
byte address also then, we say that word
locations are unaligned
Word Alignment
BaroAqoon.com

## Slide 6: Memory Operation
Load (or Read or Fetch)
Copy the content. The memory content doesn’t change.
Address – Load
Registers can be used
Store (or Write)
Overwrite the content in memory
Address and Data – Store
Registers can be used
BaroAqoon.com

## Slide 7: “Must-Perform” Operations
Instruction and Instruction Sequencing
Data transfers between the memory and the processor registers
Arithmetic and logic operations on data
Program sequencing and control
I/O transfers
BaroAqoon.com

## Slide 8: Register Transfer Notation
Identify a location by a symbolic name standing for its hardware binary address (LOC, R0,…)
Contents of a location are denoted by placing square brackets around the name of the location (R1←[LOC], R3 ←[R1]+[R2])
Register Transfer Notation (RTN)
BaroAqoon.com

## Slide 9: Assembly Language Notation
Represent machine instructions and programs.
Move LOC, R1 = R1←[LOC]
Add R1, R2, R3 = R3 ←[R1]+[R2]
BaroAqoon.com

## Slide 10: Basic Instruction Types
High-level language: C = A + B
Action: C ← [A] + [B]
Assembly: Add A, B, C
Three-address instruction: Operation Source1, Source2, Destination
Two-address instruction: Operation Source, Destination
Add A, B = B ←[A] + [B]
BaroAqoon.com

## Slide 11: Basic Instruction Types Cont…
Need to add something to the above two-address instruction to finish: Move B, C = C ← [B]
One-address instruction (to fit in one word length)
Accumulator: Add A
Load A
Add B
Store C
Zero-address instructions (stack operation)
BaroAqoon.com

## Slide 12: Using Registers
Registers are faster
Shorter instructions
  The number of registers is smaller (e.g. 32 registers need 5 bits)
Potential speedup
Minimize the frequency with which data is moved back and forth between the memory and processor registers.
BaroAqoon.com

## Slide 13: Using Registers
Load A, Ri
Store Ri, A
Add A, Ri
Add Ri, Rj
Add Ri, Rj, Rk
Move Source, Destination
Move A, Ri = Load A, Ri
Move Ri, A = Store Ri, A
BaroAqoon.com

## Slide 14: Using Registers
C=A+B
In the processors where arithmetic operations are allowed only on operands in register Move A, Ri Move B, Rj Add Ri, Rj Move Rj, C
In the processors where one operand may be in the memory but the other one must be in registers Move A, Ri Add B, Ri Move Ri, C
BaroAqoon.com

## Slide 15: Instruction Execution and Straight-Line Sequencing
B,R0
A,R0
i
+ 8
Begin execution here
Move
i
Contents
Address
C
B
A
the program
Data for
segment
program
3-instruction
Add
i
+ 4
Assumptions:
- One memory operand
per instruction
- 32-bit word length
- Memory is byte
addressable
- Full memory address
can be directly specified
in a single-word instruction
Two-phase procedure
Instruction fetch
Instruction execute
BaroAqoon.com

## Slide 16
END
BaroAqoon.com
Lecturer : Hussein Hamud Mohamed